# Personnel Steel Door Specification L20

# AspireGroup 360 single, leaf and half and double doorset

# LEAF

# 45mm thick Door leaf with flush lipped astragal (astragal only on double doors) constructed from:

- 2 no. 1.2 mm thick zinc coated steel sheets, which are welded together

- 5 no. reinforcing perimeter channels

- 42.6 mm thick dufaylite honeycomb core

FRAME

- Manufactured from 1.5 mm thick zinc coated steel

- Single rebate 95mm wide frame

- A minimum of four fixing points are provided to each jamb

- bolted top corner joints

- 100mm, 200mm, 250mm are available upon request

- Wrap around frame 85mm, Sleek frame 50mm, Tap and slot 75mm are available upon request

# DOOR IRONMONGERY

- EN1935 11-13 stainless steel, twin shrouded bearing template drilled butt hinges with integral security dog bolts are fitted as standard with CE marking

- Refer schedule for balance of ironmongery

VISION PANELS (Optional)

- Single and Double glazed in various sizes

- 6mm Laminated / 6mm Pyrocet

- 24mm Double Glazed units

LOUVRES (Optional)

- 50% Ventilation in various sizes

# FINISH

# Comes as standard powder coated

- Textured, Stainless steel, Anti-graffiti are available up on request

- Marine Grade finish is available as an option in salt laden coastal or high chlorination locations.

- Food Safe finish is available as an option

# THRESHOLD (Optional)

# 95mm wide Aluminium threshold with neoprene seal on external outward opening doors

- Ramped threshold for External inward opening doors with drip cill

# SEALS (Optional)

# 188s standard tear drop seal

# SIDEPANELS & OVERPANELS (Optional)

# Solid, Glazed and Louvred  side and overpanels available in a fixed or removable arrangement.

# MANUFACTURER

AspireGroup360

Unit 4, Fields New Road,

Chadderton,

Oldham,

OL9 8NH

Email: info@aspiregroup360.com

Web: www.aspiregroup360.com